## Slide 1: Synchrotron Radiation for Material Analysis
M. Aslam Baig
National Center for Physics
Quaid-i-Azam University Campus, Islamabad
Pakistan
aslam@ncp.edu.pk baig@qau.edu.pk

## Slide 3
X-ray ray tubes
0.02
0.04
0.06
0.08
0.10
Wavelength (nm)
Intensity (a. u.)
K
K
min
Characteristic
radiation
Bremsstrahlung
radiation
The spectrum from an X-ray tube has discrete fluorescent lines superimposed on
the continuous bremsstrahlung radiation
Anode
Vacuum tube
Cathode
Electrons
HV
Filament supply
X-rays

## Slide 4: Energy Dissipation

## Slide 5: How a Storage Ring Works

## Slide 6
Radiation angular distribution (a) electrons travelling at low speed
(b) electrons travelling at relativistic speed (g = (1-v2/c2)-1/2  10000 at ESRF)
Synchrotron radiation angular distribution
Electron orbit
Acceleration
v << c
v  c
Electron orbit
Acceleration
e-
e-
Q  m0c2/E
= 1/g rad
m0 = electron mass
v = electron velocity
E = electron energy
c = velocity of light
v
v

## Slide 8
Time structure
t
I
1ms
100 ps
e-
e-
e-
e-
Time pulsed emission is interesting for studying rapid reactions
Light pulses

## Slide 9
Als-Nielsen Introduction to Modern X-ray Physics
Synchrotron storage ring
Spectrometer
Monochromator
Undulator
300 m
Focusing
device
10 m
2 m
30 m
From the magnetic device to the experimental station
5 m

## Slide 10: Why is wavelength important?
Why is it special?
Visible light
X-rays
To penetrate a sample, you need a wavelength of similar, or smaller magnitude.
sample
sample

## Slide 11
Detector
Sample
X-rays
Absorption
X-rays
Sample
I
wavelength
Fluorescence
Imaging
Detector
X-rays
Elemental analysis
8800
0.0
8800
9000
9200
9400
9600
9800
10000
1.0
2.0
E (eV)
9000
9200
9400
9600
9800
10000
Energy
m
Detector

## Slide 12
The absorption coefficient μ
t
I = I0 exp(-μt)
linear absorption coefficient
α = μt = ln ( I0/I )
I0
I

## Slide 13
X-ray
Absorption
Fine
Structure
Zinc K-edge

## Slide 14: Extended X-ray absorption fine structure (EXAFS)
In condensed matter the ejected photo-electron (wave) will be scattered by neighbouring atoms.
It is the interference between the outgoing electron and the back-scattered ones which leads to oscillations visible in the absorption
spectrum above the edge.

## Slide 15: Extended X-ray absorption fine structure (EXAFS)
Lab data took over 12 hours to collect.
Synchrotron data took 25 minutes and could have been collected in about 3.

## Slide 16
Taken from:
“Introduction to Powder Diffraction”
By: R J Cernik
Daresbury Laboratory

## Slide 17
Powder Diffraction

## Slide 18
XANES can be used simply as a fingerprint of phases and oxidation state.
Fe compounds

## Slide 19: FLASH – Light Source

## Slide 20: Photoionization of Neon
Richter et al PRL 102, 163002, 2009

## Slide 21: Xenon Ions

## Slide 22
Bi1.7 Pb0.4 Sr2 Ca2 Cu2 O4
0
100
200
300
0.0
3.0
6.0
CaO
SrCaO2
Cu2O
Pb/Bi
Ca2CuO3
Sr
SrO
Ca
Mg
Mass / charge (m/q)
Rel. Signal Intensity (arb. units)
Surface analysis of superconducting materials
Baig et al J.Appl. Phys. 2009

## Slide 23: Future…….
Prospects for Pakistan
SESAME
Synchrotron Radiation Facility being built in Amman, Jordan